## Slide 1: 0x10B – Threat Modelling
ECED4406 – Computer Security
Dr. Colin O’Flynn
Dalhousie University.
(NOTE – This slide set is new for 2023. You can see some of this material in slides “0x301” in the old set)

## Slide 2: More Reading Reference
These slides are covered in Chapter 1 of “Hardware Hacking Handbook”.

## Slide 3: Why Threat Model?
Example: Installing a Door Lock, how secure should it be?

## Slide 4
Which lock to choose!?

## Slide 5: Parts of the Threat Model

## Slide 6: Parts of Threat Model: Assets
The end goal of attacks is accessing some sort of asset.
The asset may be obvious or non-obvious, for example:
  Credit card data (point of sale terminal).
  Access to computer system (ransomware, launching other attacks).
  Access to company data (leaking data or IP theft).
  Personally Identifiable Information (PII).

## Slide 7: Parts of Threat Model: Countermeasures
Countermeasures reduce the likelihood of a given attack being successful. Countermeasures may do any (or all) of the following:
Protect against an attack.
Detect an attack.
Respond to a detected attack.

## Slide 8: Parts of Threat Model: Attacks
Attacks are how attackers compromise a system.
Understanding the attacks is a key part of this class (you’ll learn how to apply attacks & what is required for them).
Will need to understand the complexity of attacks.

## Slide 9: Parts of Threat Model: Attackers
Attackers are the “bad actors” attacking the system.
Attackers often are rated on their knowledge & access to resources.

## Slide 10: Attack Trees
In Front of Door
Behind the Door
Attackers
Rounded boxes indicate the states an attacker is in or assets an attacker has compromised (“nouns”)

## Slide 11: Attack Trees
In Front of Door
Behind the Door
Attackers
Pick the Lock
Guess the PIN Code
Steal a key
Kick door in
Turn the handle
Open Door
Valuables
Square boxes indicate successful attacks the attacker has performed (“verbs”)

## Slide 12: Attack Trees
In Front of Door
Behind the Door
Attackers
Pick the Lock
Guess the PIN Code
Steal a key
Kick door in
Turn the handle
Open Door
Valuables
Dashed lines/arrows indicated countermeasures.
Door Lock

## Slide 13
More complex example (Figure 1-12 in book).
Shows how you can have both an Identification phase & an Exploit phase.

## Slide 14: Scoring Attack Paths
Attacks are often scored based on:
  Cost/Complexity of Identification Phase
  Cost/Complexity of Exploit Phase
  Impact of attack (may depend on usage)
  Access level required by attack
  Scalability

## Slide 15: Scalability?
Scalable attacks can be replicated by less sophisticated attackers.
In many cases these are packaged & sold.
  E.g., Console modchips (photo to right)
  E.g., automotive theft tools (https://www.vice.com/en/article/7kz48x/guy-selling-relay-attack-keyless-repeaters-to-steal-cars )

## Slide 16: Threat Scoring
Normally there is some “number” assigned to a given threat. For example:
  CVEs (Common Vulnerabilities and Exposures) have a CVSS (Common Vulnerability Scoring System)
E.G, let's look at https://nvd.nist.gov/vuln/detail/CVE-2017-0143
(WannaCry ransomware attack from 2017)
Focus mostly on the base scores for the next part…

## Slide 17: Scoring Method - CVSS

## Slide 18: Threat Models in Industry
Threat models often matched with a protection profile, which specifies certain features a given device needs to have to protect against expected threats.
In embedded systems, you can see examples of these in the Arm Platform Security Architecture (PSA) Level 1 / 2 certifications.
They originated from higher-security assurance level system used for credit cards, satellite TV cards, etc.

## Slide 19: Summary
Threat modelling may require some off-the-wall thinking to cover every possible threat.
Need to track countermeasures that exist within the system.
Can split it into both an identification & exploitation phase in more complex attacks.
Variety of industry-specific scoring methods, all generally use a similar idea of ranking difficulty of attack, impact, and how easy/scalable attack is.