## Slide 1: 0x406 – Buffer Overflows & Lab Instructions
ECED4406 – Computer Security
Dr. Colin O’Flynn
Dalhousie University.

## Slide 2: More Resources on Buffer Overflow Attacks
Original article, “Smashing the Stack for Fun & Profit”:
https://inst.eecs.berkeley.edu/~cs161/fa08/papers/stack_smashing.pdf
Blended attack exploits also an early ref:
https://courses.cs.washington.edu/courses/cse484/14au/assignments/blended.attacks.pdf

## Slide 3: What is a Buffer?
…you should know this by 4th year CE….

## Slide 4: What is a Buffer Overflow?
Writing data beyond the expected end point
Typically means you may have:
  Data corruption
  Control flow changes
  Crashes (most likely!)

## Slide 5
Function Arguments
Saved Return Address
Saved Frame Pointer
Local Variables
Function Arguments
Saved Return Address
Saved Frame Pointer
Local Variables
Stack Growth Direction
Stack Pointer
Higher Address
Lower Address
Stack Frame

## Slide 6: Function Setup
Function Arguments
Saved Return Address
Saved Frame Pointer
Local Variables
Stack Pointer

## Slide 7: ARM Important Registers

## Slide 8: e.g., when returning from function Using “bx lr” instruction

## Slide 9: e.g., when returning from function Using “pop” instruction

## Slide 11: Code Flow Execution Attacks
If we could control the return value – could we not jump anywhere?
Function Arguments
Saved Return Address
Saved Frame Pointer
Saved Return Address
Saved Frame Pointer
Local Variables
Example: Jump to somewhere in the previous function stack (maybe a buffer we wrote code to?)

## Slide 12: Shellcode In Buffer
Requires us to write shellcode into a buffer
Requires that we:
Know the location of the buffer.
Know something about the stack layout.
Can write & execute code from the buffer.

## Slide 13: Return Oriented Programming (ROP)
We could also string together existing functions
Function Arguments
Saved Return Address
Saved Frame Pointer
Function Arguments
Saved Return Address
Saved Frame Pointer
Malicious Stack Frames (maybe hundreds or thousands!)
We write a code out of small existing functions we know the address of.

## Slide 14: ROP vs. Shellcode
With ROP we are executing from valid addresses
Works even if memory is not executable

## Slide 15: Protection Methods
GCC Stack Protector (You will explore in Assignment 2)
Write a known value to the stack
Check this value is the same before returning from the function

## Slide 16: Protection Methods: Continued
Memory-Safe Languages, e.g.:
  Rust
  Python
  ..many more
Buffer Data
Buffer Metadata

## Slide 17: Protection Methods: Continued
Non-Executable Code Sections
Buffer Data
Code Data

## Slide 18: Slightly Insane Protective Methods
https://en.wikipedia.org/wiki/Intel_iAPX_432
https://homes.cs.washington.edu/~levy/capabook/Chapter9.pdf

## Slide 19: Ozone Introduction
This Ozone when googling it

## Slide 20: STM32 Nucleo Board in “J-Link Mode”
Debugger
Target

## Slide 21: Ozone with Debug Symbols

## Slide 22: What you will see

## Slide 23: Brief Intro to Ozone: Stepping
Go (Run)
Or
Pause (when running)
Reset
Step
Over
Step
Into
Step
Out

## Slide 24: Brief Intro to Ozone: Memory

## Slide 25: Brief Intro to Ozone: Memory
You can go to any memory address, even invalid ones. If you see “-” you might be on invalid memory.
Memory is NOT updated when running – need to pause the program to do that.

## Slide 26: Registers

## Slide 27: Registers
Be sure to expand (+) these so you see “Core” registers.

## Slide 28: Registers & Memory Jumping
Show code
Show data (useful for stack!)

## Slide 29: Breakpoints (Data & Code)
Right click
Example: Breakpoint on UART2 peripheral setup

## Slide 30: Breakpoints (Data & Code)

## Slide 31: Breakpoints (Data & Code)
0x40004400 + 0x04 = 0x40004404

## Slide 32: Running into Breakpoint

## Slide 33: Enabling/Disabling Breakpoints
Uncheck the box to disable – handy when you don’t want it to trigger as only want it after something like your user input

## Slide 34: Running Python Programs
Can run "raw" Python programs, but for evaluations interactive can be useful
We'll use this with ChipWhisperer on the final (4th) lab

## Slide 35: Python & ChipWhisperer

## Slide 36: Python & ChipWhisperer

## Slide 37: Running Jupyter Tutorials
Run highlighted block
Shift-Enter runs and moves to next.
Ctrl-Enter runs and stays on cell.

## Slide 38: What is Jupyter?
Interactive Python 3! Many advantages:
  Can move to “pure” Python easily afterwards.
  During development, interactive nature makes discoveries easier.

## Slide 39: Jupyter is not Perfect
Hidden state problems.
People don't ship notebooks with requirements.txt, etc.
No testing/linting that's any good built-in.
Very useless code completion (have to run the cell first, etc.).
Can't take advantage of type hints.
Several other things.

## Slide 40: Lab #3 & Assignment #2
You will cover this in Lab #3 (groups allowed) + Assignment #2 (Individual)
In Lab #3 perform a buffer overflow and inspect the running hardware.
In Assignment #2 investigate buffer overflow prevention methods and related topics (to be completed individually).
You can choose to install Ozone on your computer or complete in the lab.